LaserCutter @ Bitraf
BSU: Basic, Safe Usage
WIFI:
bitraf
grimbadgerassault
Full documentation
https://bitraf.no/wiki/Laser

---
Workshop goal
Everyone
 a) Educated in Basic Safe Usage
b) Comfortable using lasercutter
 with no/minimal assistance

---
Workshop setup
Introduction to laser. Talk 15 mins
How to use. Demonstration, 30 mins
Individual hands-on usage

---
Bitraf lasercutter Access
Members only
Requires course (this!)
Personal/prototyping: Free
Commercial jobs: 350kr/hour + tax
http://bitraf.no/join

---
Laser operating principle
Infrared laser beam burns material
Works from the top (XY)
Laser is focused to a point (using Z axis)
Cut or engrave (raster/vector)
Fundamentally mostly 2d

---
What can it be used for?
Structural
Decorative
Textiles
Signage

---
Compared to CNC mill
Tool not mechanically touching workpiece
+ Quicker setup time
+ Less bits/settings
- Limited in materials
- Poor control over depth/3d
- Slower on big parts
= Easier, but less flexible

---
Compared to 3d-printer (FDM)
Subtractive (removes) instead of additive
+ More materials
+ Bigger workarea, faster
+ Very precise 2d shapes
- 3d must be built from 2d pieces
=

---
Safe materials
Non-toxic, not catch fire, give nice finish
Typical
- Acrylic, light woods
- Paper, cardboard
- Textiles, leather
  Unsafe: plastics w/chloride (PVC, vinyl)
[Speaker Notes: Fibreboard (MDF, Poppel, Flyfiner)]

---
Getting materials
- Left-overs in workshop
- Buy in Bitmart: Acrylic, Poppel
- Pro: Oslo Fineerfabrikk, Plastkompaniet
- Quick: Clas Ohlson, Biltema
  Check wiki! https://bitraf.no/wiki/Laser

---
Basic process
- Design → export .DXF.
- Prepare toolpaths. On laser PC
- Run job
  - Insert material
  - Run Autofocus
  - Choose job Origin

---
Safety
- Fire
- Toxic materials